| Step No. | Process Step | Hazard | Type | Control Measure | CCP | Critical Limit | Monitoring Procedure | Corrective Action | Comments/ Responsibility |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | Purchasing New Vehicles/ Trailers | Goods become contaminated because of residues from Manufacturing the Vehicle | Pr | Vehicle / Trailer pressure cleaned and sanitised and inspected for physical hazards before use | No | Visually Clean load carrying area before use | As Control measure Record to be retained of cleaning before use | Do not use if not visually clean | Transport manager/office to retain records. |
| 2 | Hiring or purchasing second hand vehicles/ trailers | Goods contaminated because vehicle/trailer has previously carried Forbidden/Exclusion List Materials | Pr | Written declaration obtained from previous operator/hire company | No | Only use Vehicle / Trailer with valid declaration | Check declaration is received and valid for vehicle/trailer operated | Do not use Vehicle/Trailer without valid declaration | Module for trailer hire companies to improve assurance of Vehicle/Trailer Transport manager/office to retain records |
| 3.1 | Allocation to Vehicle/Trailer | Goods contaminated because vehicle/trailer has previously carried Forbidden/Exclusion List Materials | Pr | Goods allocated to TASCC Vehicles Trailers only | No | Only allocate to approved trailers | Check against TASCC inventory for TASCC approved trailers Check AIC Haulage Exclusion List | Reallocate to non TASCC Vehicle/Trailer, if TASCC Vehicle/Trailer has carried Forbidden/Exclusion List Material must not in future carry TASCC Goods Notify TASCC and update the TASCC inventory | Further information can be obtained from AIC Trade Assurance Helpline 0870 3000 532 |
| 3.2 |  | Goods become contaminated because vehicle/trailer not suitably equipped | Pr | Vehicle/Trailer inspected by driver on daily basis and prior to loading | No | Visually Sound and Clean Sheet and Grain Sock | As Control Measure, substandard equipment recorded in Defect Book | Do not load Vehicle/Trailer and repair damaged Load Sheet/Grain Sock before loading | Driver responsibility |
| 3.3 |  | Goods become contaminated because previous loads carried are not compatible with goods to be delivered | Pr | Transport Manager/Driver aware of specific customer requirements | No | Only goods compatible in previous loads | Driver checks three previous loads carried before loading vehicle/trailer Training completed for transport manager/drivers | Do not load vehicle/trailer, allocate to alternative vehicle/trailer | Inform customer if goods have been loaded and agree corrective action Allergens, GM Organic, NOPS etc. to be considered |

| Step No. | Process Step | Hazard | Type | Control Measure | CCP | Critical Limit | Monitoring Procedure | Corrective Action | Comments/ Responsibility |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 4 | Allocation to Driver | Driver has not received Training or is competent in the carriage of Crops/Animal Feed | Pr | Transport Manager provides Training and assesses Driver Competence at least annually | No | Competent drivers | Transport manager continually reviews Drivers Competence | Repeat Driver Training or allocate to alternative Driver | Interactive Learning Module provides mechanism of completing training |
| 5 | Allocation to Haulage Subcontractor | Haulage Subcontractor not aware of Food/Feed Hygiene requirements | Pr | Allocate to TASCC Certified Haulage Subcontractor or equivalent scheme | No | Assured Hauliers only | Check Assurance status | Allocate to alternative assured Haulier | List of equivalent schemes on AIC TASCC Website |
| 6.1 | Pre loading inspection | Goods become contaminated because vehicle/trailer load carrying area is dirty or wet | Ph Bi Ch | Driver inspects load carrying area to ensure suitably clean/dry | No | Visually dry and clean | Training completed for transport manager/drivers As control measure, record of inspection and cleaning maintained by driver | Driver cleans, dries or disinfects before loading vehicle/trailer | Transport Manager checks inspection, cleaning and disinfection records maintained. See IDTF |
| 6.2 |  | Goods become contaminated because previous loads are not compatible with goods to be delivered | Ph Bi Ch | Transport Manager/Driver aware of specific customer requirements | No | Only goods compatible in previous loads | Training completed for transport manager/drivers Driver checks three previous loads carried before loading vehicle/trailer | Do not load vehicle/trailer, allocate to alternative vehicle/trailer | Inform customer if goods have been loaded and agree corrective action Allergens, GM Organic, NOPS etc. to be considered |
| 6.3 |  | Traceability not maintained because Vehicle/Trailer not identified with Assurance Number and Trailer Number | Pr | Driver inspects Vehicle/Trailer for correct identification | No | Identified both sides and rear | As control measure | Correctly identify Vehicle/trailer before loading | Transport Manager must ensure that Vehicle Inventory is up to date and forwarded to Certification Body |
| 7.1 | Cleaning and sanitising | Goods become contaminated because of development of Biological hazard e.g. Salmonella, E-Coli etc. | Pr | Load carrying areas of Vehicles/Trailers sanitised at least every six weeks or as required in IDTF | No | Minimum six weekly or weekly sanitising | Transport Manager checks sanitising records | Disinfect vehicle/trailer before loading | See IDTF and confirm Customer requirements. |
| Step No. | Process Step | Hazard | Type | Control Measure | CCP | Critical Limit | Monitoring Procedure | Corrective Action | Comments/ Responsibility |
| 7.2 | Cleaning and sanitising | Goods become contaminated because sanitisers not Food Grade specification | Pr | Transport Manager obtains Data Sheet confirming Disinfectant/Cleaner suitable for food contact areas | No | Only food Grade Chemicals acceptable | Operator checks container of Disinfectant / Cleaner to ensure Food Grade Specification | Obtain Food Grade chemical, do not use vehicle/trailer until steam cleaned. | Product data Sheet from Suppliers contain specification if unsure contact AIC Helpline |
| 8.1 | Collection & Delivery | Incorrect goods loaded and delivered | Pr | Driver supplies load point with collection/delivery ticket detailing the correct goods | No | Always provide Collection/ Delivery Ticket | Training completed for transport manager/drivers Driver checks that the good loaded and delivered are the same as described on Collection ticket | If incorrect goods loaded or delivered, customer informed and corrective action agreed. | This includes controls for GM, Organic, Allergens, NOPS and Appendix 1 & 2 Materials e.g Stone/Recycled Stone |
| 8.2 |  | Hazardous contaminants identified in goods by driver at Collection Point | Pr | Driver inspects goods during the loading process | No | No visible hazardous contaminant | As control Measure | Driver informs Transport Manager and/or Customer | Agreed Corrective Action must not allow contaminated goods to be delivered unless agreed by Customer |
| 8.3 |  | Non Assured UK Crops delivered as Assured | Pr | Supplier provides Crop Passport with current Assurance sticker | No | Must have assurance sticker | As control measure | Driver informs Transport Manager and/or Customer | Can be delivered as Non Assured, |
| 8.4 |  | Goods become contaminated because Driver or Loader walks on loads with dirty footwear/clothing | Pr | If absolutely essential ensure footwear/clothing will not contaminate goods | No | Visibly Clean footwear /clothing | As control measure | Driver obtains permission from Transport Manager and/or Customer before walking on loads | Driver must comply with site Health and safety policies and rules |
| 9 | Rejection | Redeliver rejected Goods containing Hazardous Impurities to Food/Feed destination | Pr | Customer and Transport Manager informed of rejected goods which contain Hazardous Impurities | No | Absence of Hazardous Impurities | Records of rejection are attached to Collection Delivery Ticket | Driver obtains instructions from Transport Manager and/or Customer before redelivering loads. | All rejections reported to Customer |

(Bi) Biological (Ch) Chemical (Ph) Physical Hazard (Pr) Prerequisite

Hazardous Impurities

| Hazardous impurities can be identified in goods at a number of process steps both by Drivers or by Suppliers, Customers or Haulage Contractors. In all of these cases the Transport Team have a legal responsibility once they are aware of the potential contamination to ensure that these goods do not enter the Food/Feed Chain. Hazardous Impurities can take a number of forms but are categorised below in three distinct categories: Physical, Chemical or Biological. |
| --- |
| Physical |
| Type of Contamination | Corrective Action |
| Metal | Depending on the type of metal the goods can be cleaned/conditioned and returned for Feed/Food use, the Transport Team obtain sample to establish whether goods can be cleaned/conditioned, otherwise goods are returned to the supplier or Delivered for Non Food/Non Feed Use |
| Glass & Hard Plastics | Goods are returned to Supplier or Delivered for Non Food/Non Feed Use |
| Mud Balls, Stones and Flint | Depending on the type of contamination the goods can be cleaned/conditioned and returned for Feed/Food use, the Transport Team obtain sample to establish whether goods can be cleaned/conditioned, otherwise Goods are returned for Farm or Delivered for Non Food/Non Feed Use |
| Bitumen and Tarmac | Goods are returned to Supplier or Delivered for Non Food/Non Feed Use |
| Chemical |
| Rodenticide, Chemically Treated Seed | Goods are returned to Supplier or Delivered for Non Food/Non Feed Use |
| Diesel/Oil | Goods are returned to Supplier or Delivered for Non Food/Non Feed Use |
| Biological |
| Ergot | Depending on the type of contamination the crop can be cleaned/conditioned and returned for Feed/Food use, the Transport Team obtain sample to establish whether crop can be cleaned/conditioned, otherwise Crops are returned to farm or redelivered to Customers who have confirmed they except Ergot as an impurity or for non Food/Feed use |
| Allergens List of Allergens contained in Appendix 2 AIC TASCC Code of Practice | Crops that are delivered for food are contaminated with a product potentially causing an allergic reaction, these include Nut and Nut Products, Sesame Seeds etc. but may also be found in Biscuit Meal, Confectionery Waste and Cattle Blend. Crops contaminated with these products are not delivered for Food use but may be Delivered for Feed Use, Returned to the Supplier or for other non Food uses. |
| Mycotoxin Don, Zea, OTA | Crops exceeding the MPL for Food can be redelivered for Feed use or returned to supplier |
| Salmonella | Goods are returned to Supplier or Delivered for Non Food/Non Feed Use |
| Live or dead Animals | Goods are returned to Supplier or Delivered for Non Food/Non Feed Use |
| Faeces, Vermin Droppings | Goods are returned to Supplier or Delivered for Non Food/Non Feed Use |

The above table provides a summary of Hazardous impurities there may be others types of contamination or where the contamination is severe. In each case the Transport Team must inform the Customer/Recipient who complete a Risk Assessment to determine the appropriate corrective action. In all cases when a contamination is established the Corrective Action taken by the business is recorded on the Collection/Delivery Ticket together with the eventual destination of the goods.

In some cases Customer/Recipients confirm that they are prepared to accept goods contaminated with hazardous impurities for Food/Feed uses. On no account should contaminated goods be delivered unless confirmation is received in writing prior to delivery from the Customer/Recipient.